## Slide 1: FNAL update tracking results for CMS SS detector
A. Zhang, V. Bhopatkar, M. Hohlmann,
M. Phipps, J. Twigger
Florida Institute of Technology
24/03/2014

## Slide 2
Our strategy :
Measure the angular angle: 9.94° (173.5mrad), angle pitch is 0.453mrad.
Measure the physical range of offset in X, should be in (1800,1900) (mm).
Iterating on X and Y offsets, record track in ϕ and r, residual sigma and mean on CMS GEM sector 5 .
Check the relationships to find an optimized (X, Y) offset.
Rotation angle of the detector can also be optimized.
Tracking fitting was done with CMS detector included.
This study is for CMS detector with straight strip r/o.
REF
Det.
X
offset
CMS
Eta5
origin
vertex
~9.94°

## Slide 3: Optimization of X,Y offsets (Inclusive)
Track Χ2 in ϕ versus X @ Y=-30
Track Χ2 in ϕ versus X @ Y=-28
Track Χ2 in ϕ versus X @ Y=-29
Look at track χ2 in ϕ in versus X offset, only between Y at -28mm and -30mm, it shows a parabolic curve. (Y beyond that range gives bad curves)
Y=-29mm is taken as the optimized offset, fit this curve, then we get optimized X offset at -1864mm.

## Slide 4: Residual distributions after optimization
Track Χ2 in ϕ versus Y @ X=-1864mm
Minimum point
gives Y=-29.1mm
Rotation angle is optimized ~ 28 μrad
Inclusive residual
Exclusive residual
CMS GEM sector 5,
HV 3250V
σ= 93μrad
σ= 118μrad
Resolution
(geom. mean):
104μrad,
or 193μm

## Slide 5
events from the first 20k raw events
events from the first 40k raw events
Phi_REF2_vs_phi_Eta5
Residual_Eta5
From one of our high statistic data